|  | State of New Mexico Energy Minerals and Natural Resources Oil Conservation Division 1220 South St. Francis Dr. Santa Fe, NM 87505 | Form C-122-A Revised June 10, 2003 |
| --- | --- | --- |

WELL DELIVERABILITY TEST REPORT FOR YEAR 20___

| Pool Name | Pool Slope n = | Formation | County |
| --- | --- | --- | --- |
| Operator | Well Name and Number |
| Unit Letter | Section | Township | Range | Purchasing Pipeline |
| Casing O.D. – Inches | Casing I.D. – Inches | Set at Depth – Feet | Tubing O.D. - Inches | Tubing I.D. – Inches | Top – Tubing Perf. - Feet |
| Gas Pay Zone From To | Well Producing Thru Casing Tubing | Gas Gravity | Gravity X Length |
| Date of Flow Test From To | Date Shut-in Pressure Measured |
| PRESSURE DATA – ALL PRESSURES IN PSIA |
| (a) Flowing Casing Pressure (DWt) | (b) Flowing Tubing Pressure (DWt) | (c) Flowing Meter Pressure (DWt) | (d) Flow Chart Static Reading | (e) Meter Error (Item c – Item d) | (f) Friction Loss (a – c) or (b – c) | (g) Average Meter Pressure (Integr.) |
| (h) Corrected Meter Pressure (g = e) | (i) Avg. Wellhead Press. Pt = (h + f) | (j) Shut-in Casing Pressure (DWt) | (k) Shut-in Tubing Pressure (DWt) | (l) Pc = higher value of (j) or (k) | (m) Del. Pressure Pd = _________% Pc | (n) Separator or De- hydrator Pr. (DWt) for critical flow only |
| FLOW RATE CORRECTION (METER ERROR) |
| Integrated Volume – MCF/D | Item c Quotient of __________ Item d | Item c __________ Item d | Corrected Volume Q = MCF/D |
| WORKING PRESSURE CALCULATION |
| (l – e –a) | (FcQm)2 (1000) | R2 = (l – e –a) (FcQm)2 (1000) | Pt2 | Pw2 = Pt2 + R2 | Pw = Pw2 |
| DELIVERABILITY CALCULATION |
| n n Pc2 – Pd2 n D = Q ________ = Pc2 – Pw2 ________________ __________________ = _____________________ = ________________ = ___________________MCF/D |
| REMARKS: |
| SUMMARY | Company: |
| Item: | h _______________________________________ Psia | By: |
|  | Pc ______________________________________ Psia | Title: |
|  | Q _____________________________________ MCF/D | E-mail Address: |
|  | Pw______________________________________ Psia | Witnessed By: |
|  | Pd______________________________________ Psia | Company: |
|  | D ______________________________________ MCF/D | E-mail Address: |